## Slide 1
BIS Standards Recommendation Engine
Team BrainFreeze
GitHub code link: https://github.com/eesha-kamath/bis-standards-recommendation-engine
Demo video link: https://youtu.be/yuJFtrS6XGI

## Slide 2
BIS Standards Recommendation Engine
100%
Hit Rate @3
1.0
MRR @5
0.03s
Avg Latency
Hybrid BM25 + TF-IDF search over SP 21 building materials standards
Target: Hit Rate >80%, MRR >0.70, Latency <5s All 3 exceeded

## Slide 3
Solution Overview
Parse SP 21
569 IS standards pulled from 929 pages. Regex header detection. Longest entry kept to skip table of contents stubs.
Hybrid Search
BM25 for exact keyword match plus TF-IDF trigrams for phrase overlap. Fused 50/50. No GPU. No neural model.
Query Expansion
30 domain shortcuts expanded before search. OPC becomes Ordinary Portland Cement. SRPC becomes Sulphate Resisting. Etc.
No Hallucinations
3 independent guards: LLM only sees 8 candidates, prompt blocks invented codes, code validation drops anything not retrieved.

## Slide 4
System Architecture
BUILD - runs once
SP 21
PDF
929 pages
›
Extract
Text
pdftotext
›
Parse +
Dedup
569 standards
›
Alias
Enrich
18 IS codes
›
Build
Index
BM25 + TF-IDF
QUERY - every search
Product
Description
plain English
›
Expand
Query
30 aliases
›
BM25 +
TF-IDF
fused score
›
Top 8
Candidates
retrieved
›
Llama 3.3
Rationale
via Groq API
›
Validate
Output
no hallucination
OUTPUT Top 3 to 5 IS Standards Rationale Confidence Score Compliance Checklist
No LLM mode: fully offline, 0.03s response, no API key needed
With Groq API: Llama 3.3 generates plain English rationales, under 3 seconds

## Slide 5
Chunking and Retrieval Strategy
How we parsed SP 21
1
IS Header Detection
Regex finds every IS XXXX : YYYY block. 569 standards extracted.
2
Drop Table of Contents Stubs
PDF has short TOC entries for every standard. We keep only the longest version, which is always the full summary.
3
Alias Injection
18 key standards get trade names added directly. IS 269 gets OPC 33. IS 455 gets PSC. Closes the vocabulary gap.
4
1400 Character Cap
Each document trimmed to 1400 chars plus aliases to keep the index fast.
Retrieval Fusion
BM25
exact keyword match
TF-IDF Trigrams
phrase cosine match
▼
▼
0.5 x BM25 + 0.5 x TF-IDF = Final Score
Top 8 candidates selected
Pure numpy operations, no GPU
Sparse beats dense for IS terminology

## Slide 6
Evaluation Results
100%
Hit Rate @3
Target was over 80%
1.0
MRR @5
Target was over 0.70
0.03s
Avg Latency
Target was under 5s

## Slide 7
Demo Highlights
Retrieval only (0.04s, offline)
With Groq rationales (2.74s)
Compliance checklist tab
JSON output tab

## Slide 8
How We Score on Every Criterion
PRIMARY METRICS: Automated against hidden test set
Hit Rate @3
Target >80%
We got 100%
MRR @5
Target >0.70
We got 1.00
Avg Latency
Target <5 sec
We got 0.03s
SECONDARY METRICS: Manual review by judges
Relevance Score (10 pts)
Judge picks 5 random queries and rates our top 3 results on a 1 to 5 scale.
Our rationales are specific, sourced from SP 21, and explain exactly why each IS code applies to that product.
No Hallucinations (10 pts)
Binary check per response. Any invented IS code = 0. Score = clean responses divided by total.
We have 3 independent layers. The LLM physically cannot see or return any standard outside the 8 retrieved. Guaranteed clean.
SUBJECTIVE: Code quality, Innovation, UI, Presentation
Technical
Excellence
Clean 4-file codebase. One command runs everything. requirements.txt included.
Innovation
Hybrid sparse retrieval. Alias injection. TOC dedup fix. Offline mode. Deliberate architectural choices.
Usability
and Impact
Gradio UI, 3 tabs, confidence scores, compliance checklist. Works offline on any laptop.
Presentation
This deck. Live demo on Google Meet.

## Slide 9
Impact on MSEs and Team
Real world impact
BEFORE to AFTER with BrainFreeze
x Weeks searching BIS documents
v Seconds with a product description
x Risk of picking the wrong standard
v 3 layer hallucination prevention
x Need to understand BIS terminology
v Plain English rationales and checklists
x Need internet and paid APIs
v Offline mode on any factory laptop
Team BrainFreeze Tech Stack
► SP 21 BIS PDF (sole source)
► pdftotext (text extraction)
► rank-bm25 (keyword retrieval)
► scikit-learn (TF-IDF trigrams)
► Groq API Llama 3.3 70B
► Gradio (web UI)
► Python 3.10+ no GPU needed
One command. 0.03 seconds. The right BIS standard. Every time.